## Slide 1
CONTENT UNDER DEVELOPMENT…
sorry

## Slide 2
ACADEMIC

## Slide 3
METHODS
STEP 1- CT scans collected in a custom rig with embedded load cell
during functional tasks.
STEP 2- 3D reconstruction of the hand.
STEP 3- Design an algorithm estimating intra-articular
pressure based on a biomechanical model of the cartilage.
STEP 4- Comparison of pressure distribution patterns.
PURPOSE- develop a novel medical imaging-based approach
to measure the morphological and mechanical properties
of cartilage in vivo.
 Copyright DOURTHE TECHNOLOGIES 2019
RESULTS
Peak pressure was consistently located around the same region
of the thumb’s articular surface during power grasp.
These results may explain why degenerative changes are
usually observed around this location during the primary stages of
osteoarthritis development.
CONCLUSION- the algorithm developed for this study is a valuable tool that allows clinicians to estimate the distribution of contact pressure within joints in vivo.

## Slide 4
RESULTS
The analysis showed that thumb mobility is allowed via both
3D rotations and translation of the entire articular chain.
The fact that the thumb experiences rotations in all 3 dimensions during
thumb flexion supports the existence of a screw-home mechanism.
METHODS
STEP 1- Collect CT scans of healthy volunteers in positions of maximal
thumb extension, flexion, abduction and adduction
STEP 2- Evaluate thumb mobility using a custom-made
algorithm calculating 3D transformations between bone
models generated via CT image reconstruction
PURPOSE- develop a marker-free motion capture technique using medical imaging to assess and understand thumb mobility.
CONCLUSION- The thumb plays a significant role in basic hand function. The algorithm developed in this study offers new possibility to assess the mobility of small human joints, which would not be measurable via traditional marker-based motion capture.
TRANSFORM
THUMB MOBILITY
 Copyright DOURTHE TECHNOLOGIES 2019

## Slide 5
RESULTS
Regardless of the limited (and optimized) radiation dose used
during dynamic CT scanning, high levels of consistency and accuracy
were found when comparing motion patterns between specimen.
METHODS
STEP 1- dynamic CT scans acquired from 6 cadaveric human forearms,
while a motion simulator imposed thumb opposition.
STEP 2- 3D reconstruction of the hand for each frame using a
semi-automated segmentation algorithm.
STEP 3- technique’s accuracy assessment using the variation
in distance between silicon nitride beads.
PURPOSE- apply dynamic medical imaging to overcome the limitations of current motion capture technologies regarding the quantification of the mobility of small joints (e.g. fingers).
Silicon nitride beads
Dynamic thumb tracking
CONCLUSION- This study concluded that dynamic medical imaging technology can be used to visualize and quantify 3D thumb mobility, making it a valuable tool to assess small joints’ kinematics in vivo.
 Copyright DOURTHE TECHNOLOGIES 2019

## Slide 6
RESULTS
Distinct proximity patterns were observed across tasks with a
recurrent pattern found around a specific region of the joint.
Important joint degeneration and joint space narrowing were observed
among OA patients, leading to larger estimated intra-articular pressure.
METHODS
STEP 1- CT scans collected in a custom rig during basic thumb movements
and functional tasks.
STEP 2- 3D reconstruction of the hand.
STEP 3- Design a proximity mapping algorithm to estimate
intra-articular pressure from medical images.
STEP 4- Comparison of pressure distribution patterns
between healthy and OA subjects.
PURPOSE- better understand how degenerative joint diseases occurs by comparing pressure distribution patterns between healthy and osteoarthritic (OA) subjects.
OA
HEALTHY
CONCLUSION- This study improved our understanding of OA development by assessing how joint pressure is distributed during tasks of daily living for healthy and arthritic subject.
 Copyright DOURTHE TECHNOLOGIES 2019

## Slide 7
RESULTS
The study showed that advanced thumb OA can largely
restricts the mobility of the thumb.
It also showed that total thumb arthroplasty is able to partially restore
thumb function, but cannot fully replicate the kinematics of the healthy thumb.
METHODS
Several patients with advanced OA symptoms were tested.
STEP 1- Collect CT pre- and post-surgery scans of the patient’s affected
hand while performing thumb movements (e.g. thumb flexion)
STEP 2- Evaluate thumb mobility using a custom-made algorithm
calculating 3D transformations between bone models
generated via CT image reconstruction
PURPOSE- quantify the impact of osteoarthritis (OA) and total thumb joint replacement on thumb mobility.
CONCLUSION- The quantification of thumb mobility in OA patients pre- and post-surgery improved our understanding of the disease, and can help enhance current implant designs.
OA
IMPLANT
 Copyright DOURTHE TECHNOLOGIES 2019

## Slide 8
METHODS
STEP 1- Extract human joints samples from cadavers.
STEP 2- Measure the load-displacement behavior using cartilage custom
indentation technology.
STEP 3- Obtain contrast-enhance high resolution scans of the
samples to measure their composition.
STEP 4- Assess the correlation between cartilage
mechanical properties and composition.
PURPOSE- develop a novel medical imaging-based approach to measure the morphological and mechanical properties of
cartilage in vivo.
RESULTS
A positive correlation was found between the composition
and mechanical properties of the cartilage.
CONCLUSION- This work provides a new method for the non-destructive in vivo assessment of cartilage properties, as well as a greater understanding of cartilage behavior and a dataset for the development of more accurate computer models of human joints.
 Copyright DOURTHE TECHNOLOGIES 2019

## Slide 9
INDUSTRY

## Slide 10
VARIABLES OF INTEREST
The following variables were collected and compared across garments:
Passive/Active joint reactions | Garment compression | Peak power output | Fatigue index
BACKGROUND- Per4ma Sports Technology LTD is a Canadian company that designs compression garments with the objective to improve athletic performance and promote post-injury recovery
STUDY OBJECTIVE
Compare the Per4ma garments to a leading competitor (Under Armour) and a control condition (non-compressive garment) with respect to its effect on performance, posture, comfort and fatigue
INDUSTRY PARTNER- Per4ma Sports Technology LTD.
RESULTS ABSTRACT*
The Per4ma shirt provided more resistance during slow and fast shoulder flexion movements, which may contribute to an improved control of shoulder mobility, thereby limiting the risks of shoulder injuries
*Due to privacy restrictions, full disclosure of the study’s conclusions is not permitted
 Copyright DOURTHE TECHNOLOGIES 2019

## Slide 11
VARIABLES OF INTEREST
The following variables were collected and compared across systems:
Center of pressure trajectory| Plantar pressure distribution | Ground reaction forces
BACKGROUND- Orpyx Medical Technologies Inc. is a Canadian company that designs foot pressure measurement technologies used to improve human health and advance sports performance
STUDY OBJECTIVE
Compare the accuracy of the Orpyx LogR Gen 2 prototype to the well-established Pedar System (Novel, Germany) and a Kistler force plate (Kistler Group, Switzerland) with respect to several biomechanical variables
INDUSTRY PARTNER- Orpyx Medical Technologies Inc.
RESULTS ABSTRACT*
Comparable center of pressure trajectories and ground reaction forces were similar among the different tested systems
*Due to privacy restrictions, full disclosure of the study’s conclusions is not permitted
 Copyright DOURTHE TECHNOLOGIES 2019

## Slide 12
VARIABLES OF INTEREST
The following variables were collected and compared with a control condition:
Perceived fatigue level | Subjective comfort | EMG activity in the quad and calf muscles Foot trajectory | Arch morphology | Plantar pressure distribution
BACKGROUND- Dr. Scholl's is a footwear and orthopedic foot care brand who recently introduced the concept of self-selected customized orthotics in the market
STUDY OBJECTIVE
Three distinct studies were performed over a year-long project to quantify the impact of self-selected customized orthotics on the legs and feet during long periods of standing, as well as during regular and uphill power walking
INDUSTRY PARTNER- Dr. Scholl’s
RESULTS ABSTRACT*
The results of this study indicate some potential benefits regarding the use of
self-selected customized orthotics with respect to lower limb biomechanics
and perceived fatigue
*Due to privacy restrictions, full disclosure of the study’s conclusions is not permitted
 Copyright DOURTHE TECHNOLOGIES 2019

## Slide 13
ALGORITH
DEVELOPMENT

## Slide 14
CONTENT PREVIEW
(additional content constantly being developed)
3D TRANSFORMATIONS TOOLBOX
This toolbox includes a few custom python codes enabling
essential operations and transformations on 3D objects
Transformations between coordinate systems | Calculates the rotation and translation matrices allowing the transformations of a data set from a global to a local coordinate system (and vice versa)
Find joint centers (motion capture) | Find the coordinates of a joint center using static and dynamic motion capture data (e.g. Vicon)
Nearest (Euclidean) neighbor | Find the nearest (Euclidean) neighbor between two data sets of points.
Iterative Closest Point (ICP) | Use an ICP method to find the best-fit transform that maps points A on to points B
 Copyright DOURTHE TECHNOLOGIES 2019

## Slide 15
SIGNAL PROCESSING TOOLBOX
This toolbox includes a few custom python codes enabling
essential signal processing operations
DVJ event detection | Detect events during a drop vertical jump (DVJ) (e.g. landing, takeoff and maximal jump height)
Moving average filter | Applies a moving average filter to a time series
Cubic spline resampling | Fits a cubic spline to the data and resamples the corresponding time series to the desired sampling rate
Cubic spline fill | Assesses if time series has missing observations and interpolates using a cubic spline fitted to the data
CONTENT PREVIEW
(additional content constantly being developed)
 Copyright DOURTHE TECHNOLOGIES 2019

## Slide 16
MACHINE LEARNING PROJECTS
This repository includes a few custom python codes written to solve classification problems using convolutional neural network
CONTENT PREVIEW
(additional content constantly being developed)
 Copyright DOURTHE TECHNOLOGIES 2019
cats-v-dogs_dcnn.py | Uses a deep convolutional neural network (with data augmentation) to address the Cats v Dogs full Kaggle Challenge
horses-v-humans_dcnn.py | Uses transfer learning combined with a local deep convolutional neural network (with data augmentation) to enable a 99.9% classification accuracy using images of horses and humans
mnist\_fashion\_cnn.py | Define a convolutional neural network (with callbacks) to classify different clothing items

## Slide 17
COMPUTER VISION PROJECTS
This repository includes a few custom python codes written to
solve specific computer vision problems
img annotation | Allow the manual annotation of body landmarks by importing a data set of 2D images of people running (for validation of the automated algorithm)
CONTENT PREVIEW
(additional content constantly being developed)
 Copyright DOURTHE TECHNOLOGIES 2019

## Slide 18
DRAFTS

## Slide 19
 Copyright DOURTHE|TECH 2019

## Slide 20
Assessing thumb mobility using medical imaging
Collect CT scans
of the hand
during task
(e.g. thumb flexion)
Using
reconstructed
3D models
calculate thumb movement from position 1
to position 2
(via ICP algorithm)
Compare
mobility
between healthy
volunteers and patient affected
by a joint
condition
(i.e.
osteoarthritis)

## Slide 21
CONCLUSION- the algorithm developed for this study is a valuable tool that allows clinicians to estimate the distribution of contact pressure within joints in vivo.
PURPOSE- assess how contact pressure is distributed in the thumb joint in vivo during functional tasks and better understand how degenerative diseases such as osteoarthritis occur.
 Copyright DOURTHE|TECH 2019
METHODS
STEP 1- CT scan collected in a custom rig with embedded load cell during functional task.
STEP 2- 3D reconstruction of the hand.
STEP 3- Design of an algorithm estimating
intra-articular joint pressure based on a biomechanical model of the cartilage.
STEP 4- Comparison of pressure
distribution patterns between tasks.
RESULTS
FINDING 1- The mean contact pressure
in the thumb was similar between the neutral and lateral pinch configurations.
FINDING 2- The highest peaks in contact pressure were found during power grasp.
FINDING 3- Peak pressure was consistently located around the volar and radial regions of the thumb during power grasp.
FINDING 4- These results may explain why degenerative changes are usually observed in this location during the primary stages of osteoarthritis development.